Technical Paper

Pengaruh Pemanasan Kelapa Parut Dan Teknik Pengunduhan Terhadap Rendemen Dan Mutu Virgin Coconut Oil (VCO)

The Effects of Grated Coconut Heating and Harvesting Technique on the Productivity

and Quality of Virgin Coconut Oil

Sutardi Staf Pengajar Jurusan Teknologi Pangan dan Hasil Pertanian, I, Umar Santoso Staf Pengajar Jurusan Teknologi Pangan dan Hasil Pertanian, I dan Anggia Alumni Sekolah Pasca Sarjana, Universitas Gadjah Mada, Yoc

Abstract

Virgin Coconut Oil (VCO) was produced from green variety of non-hybride coconut type. Grated coconut was heated at 50°, 70°, and 90°C for 20, 30 and 40 minutes, respectively. Harvesting technique of VCO were done by conventional, utilization of stainless steel screen, and filter paper laminated stainless steel screen methods, respectively. Produced VCO was^stfSsequently analyzed their productivity and quality parameters consisting of moisture content, acid/cumber, free fatty acid (FFA), peroxide number, iodine number, saponification number, clearness and fatty acid profile of VCO. Statistical analysis was also conducted by using Analysis of Variance and Duncan Multiple Range Test with 5% significancy.

The results showed that heating of grated coconut at 90°C for 40 minutes produced 29.65 ± 0.38% VCO, and it was the highest productivity. Heating temperature of grated coconut and with any harvesting technique didn't statistitically have significant effect on productivity and quality of VCO. While, combination of heating temperature at 90°C and it was followed by harvesting technique using stainless steel screen produced the highest VCO i.e. 31.54 + 0.58%. The best quality of VCO was characterized by 0.09 ± 0.01% moisture content, 0.20 ± 0.02 mg KOH/g oil of acid number, 0.12 + 0.01% free fatty acid (FFA), 0.37 + 0.01 meq/kg oil of peroxide number, 5.11 ± 0.01 g iod/100 g oil of iodine number, 244.12 ± 0.01 mg KOH/g oil saponification number and the VCO was clear and transparant. Fatty acid profile of selected VCO was dominated by medium chain fatty acid (Cn o) particularly lauric acid i.e. 50.26% and followed by 8.65% caprylic and 5,73% capric acids, respectively.

The quality parameters of VCO was able to meet the quality standard of VCO that was issued by APCC (Asia Pacific Coconut Community) quality grade.

Keywords: Grated coconut, heating, harvesting technique and VCO.

Diterima: 19 April 2008; Disetujui:27 Juli 2008

Pendahuluan

Tanaman kelapa (Cocos nucifera L.) merupakan tanaman serbaguna yang memiliki nilai ekonomi tinggi. Seluruh bagian tanaman mulai dari akar, batang, daun dan buah dapat dimanfaatkan untuk pemenuhan kebutuhan manusia, sehingga disebut sebagai pohon kehidupan (tree for life). Salah satu produk olahan daging buah kelapa adalah minyak kelapa yang telah lama dibuat oleh masyarakat secara tradisional dan selanjutnya dikenal sebagai minyak klentik atau minyak krengsengan.

Dengan sentuhan teknologi maka pembuatan minyak kelapa dapat dilakukan secara cepat, praktis dan hasilmya lebih baik dengan komponen alaminya masih dapat dipertahankan dan bahkan memiliki banyak khasiat baik sebagai minyak goring maupun minyak makan fungsional. Minyak kelapa yang dibuat tanpa menggunakan panas diharapkan tidak banyak mengalami perubahan baik komponen penyusun maupun sifat fisik dan kimianya, dan minyak jenis ini lazim dikenal sebagai minyak kelapa perawan (Virgin Coconut Oil).

Sejalan dengan informasi tersebut maka metode pemanasan dalam pembuatan VCO mulai ditinggalkan. Namun demikian, pemanasan yang dilakukan terhadap kelapa parut, berbeda dengan yang telah lazim dilakukan untuk pemanasan santan untuk menghasilkan minyak goring. Selain suhu tinggi dan waktu yang relatif lama pada pemanasan santan untuk menjadi minyak, maka dipastikan merusak minyak kelapa yang dihasilkan baik secara fisik, kimiawi maupun inderawi. Pembuatan VCO dengan teknologi pemanasan kelapa parut belum pernah dilakukan. Disamping itu teknik pengunduhan VCO terkadang diabaikan, padahal teknik pengunduhan

5 UGM, Yogyakarta. 5 UGM, Yogyakarta.